## Slide 1: Digesting the Digital Twin
Cláudio Gomes, Hao Feng, Casper Thule,
Kenneth Lausdahl, Peter Gorm Larsen

## Slide 2: How do others define a Digital Twin?
Hard to pick one.
Our summary, from [2,3]:
  Digital Twin: “when the data flows between an existing physical object and a digital object […] A change made to the physical object automatically leads to a change in the digital object and vice versa.”
[1] - Barbara Rita Barricelli, Elena Casiraghi, and Daniela Fogli, “A Survey on Digital Twin: Definitions, Characteristics, Applications, and Design Implications,” IEEE Access 7 (2019): 167653–71.
[2] – Ongoing work by Til Boettjer et. al. on surveying the digital twin literature.
[3] – Fuller, Aidan, Zhong Fan, Charles Day, and Chris Barlow. “Digital Twin: Enabling Technologies, Challenges and Open Research.” IEEE Access 8 (2020): 108952–71. https://doi.org/10.1109/ACCESS.2020.2998358.

## Slide 3: Our Goal & Benefits of Digital Shadows
Physical Twin
Plant
Controller
Digital Shadow
Communication
3D Visualization
Safety Monitoring
Predictive maintenance
Fault Diagnosis
Support for decision making

## Slide 4: Our Goal & Benefits of Digital Twin
Physical Twin
Plant
Controller
Digital Twin
Communication
3D Visualization
Safety Monitoring
Predictive maintenance
Fault Diagnosis
Support for decision making
Self-reconfiguration

## Slide 5: Example Physical Twin: Plant
[1] – Full details in technical report by Hao Feng et. al.
Physical Twin
Plant
Controller
Room Temperature

## Slide 6: Example Physical Twin: Controller
[1] – Full details in technical report by Hao Feng et. al.
Physical Twin
Plant
Controller
Notes: Explain Ctrl parameters

## Slide 7: Atoms of a Digital Shadow
Physical Twin
Digital Shadow
Communication
3D Visualization
Safety Monitoring
Predictive maintenance
Fault Diagnosis
Support for decision making

## Slide 8: One-way Communication
Physical Twin
Digital Shadow
RabbitMQ
Controller
timestamp: XX
heater: on
t1: 22°C
t2: 32°C
t3: 33°C
Data Recorder
data.csv
Kalman Filter
…
Setup by Casper and Kenneth
AMQP is the protocol.
RabbitMQ is the implementation of it.
It is tested in industry for years.
Notes: Using RabbitMQ message broker
Physical twin produces timestamped messages:
Controller signals
Plant sensor measurements

## Slide 9: Visualization
Challenge: develop useful ways to display data about the Physical Twin
3D visualizations are featured in 5/7 DT papers read by Til Boettjer et. al. [2]
Out of our scope due to very specific to application.
[1] - International Atomic Energy Agency. “Control Room Systems Design for Nuclear Power Plants.” Nuclear Power Engineering Section, 1995. https://inis.iaea.org/collection/NCLCollectionStore/_Public/27/002/27002051.pdf.
[2] – Ongoing work by Till Boettjer et. al. on surveying the digital twin literature.
Notes: Develop useful ways to display data about the Physical Twin
Not just 3D visualization, but 3D visualizations are featured in many DT papers (about 5 out of every 7 papers read by Til Boettjer et. al. [2]
Out of scope, but contributions welcome!

## Slide 10: Visualization
incubator_data.html
Same framework we use in the into-cps application.
Digital Shadow
3D Visualization
Safety Monitoring
Predictive maintenance
Fault Diagnosis
Support for decision making

## Slide 11: State Estimation: Kalman Filter
Digital Shadow
Plant
Controller
Kalman Filter
Room:
Styrofoam
Safety Monitor
Predictive Maintenance
Decision Support
…
Model
Digital Shadow
3D Visualization
Safety Monitoring
Predictive maintenance
Fault Diagnosis
Support for decision making
Notes: Goal: translate what is observable from the system (temperature of the two sensors) into the state of the system (temperature of heatbed and average temperature).
  Show a diagram of this.
KF accomplishes two things:
  Fares well with noisy measurements,
  And allows us to recover the “hidden variables” of the incubator
BUT: It needs a model!

## Slide 12: Modelling Plant
Plant
Room:
Styrofoam
Model
Kalman Filter
Notes: Explain Model: inputs/outputs/parameters
dTh_dt = 1.0*(-G_heater*(-T + T_h) + V_heater*i_heater*on_heater)/C_heater
dT_dt = 1.0*(-G_box*(T - T_room) + G_heater*(-T + T_h))/C_air

## Slide 13: Parameter Estimation
Physical Twin
Digital Shadow
Controller
Data Recorder
data.csv
LSE Solver
Model
Plant
Best Parameters
calibration_results.html
Moving Average
Notes: 1. Run experiment

## Slide 14: State Estimation: Kalman Filter Results
Digital Shadow
Plant
Controller
Kalman Filter
Room:
Styrofoam
Model
kalman_results.html
Digital Shadow
3D Visualization
Safety Monitoring
Predictive maintenance
Fault Diagnosis
Support for decision making

## Slide 15: Kalman Filter vs Tracking Simulator [1]
KF runs at every sample
Needs linearization
Needs modified model
Fast (can be run real-time)
Handles noise
TS needs periodic re-calibration
Works for non-linear models and co-simulations
Estimates both parameters and states
Slow (soft real-time)
Does not handle noise
[1] - Legaard, Christian Møldrup, Cláudio Gomes, Peter Gorm Larsen, and Frederik F. Foldager. “Rapid Prototyping of Self-Adaptive-Systems Using Python Functional Mockup Units,” to appear. SummerSim ’20. Virtual event: ACM New York, NY, USA, 2020.

## Slide 16: Monitoring
Digital Shadow
Plant
Controller
Kalman Filter
Styrofoam
State
Model
Anomaly Detector
Digital Shadow
3D Visualization
Safety Monitoring
Predictive maintenance
Fault Diagnosis
Support for decision making

## Slide 17: Anomaly Detector Results
Digital Twin
3D Visualization
Safety Monitoring
Predictive maintenance
Fault Diagnosis
Support for decision making
...
Self-reconfiguration
Open Lid
Close Lid

## Slide 18: Fault Diagnosis
Digital Shadow
Plant
Controller
Kalman Filter Normal
Styrofoam
State
Model Normal
Anomaly Detector
Kalman Filter Fault
State
Model Fault
Fault Scenario Detector
Digital Shadow
3D Visualization
Safety Monitoring
Predictive maintenance
Fault Diagnosis
Support for decision making

## Slide 19: What-If (Co)-Simulations
Digital Shadow
Plant
Controller
Kalman Filter
Styrofoam
State
Model
What-If Simulation
Digital Shadow
3D Visualization
Safety Monitoring
Predictive maintenance
Fault Diagnosis
Support for decision making
Notes: Show use case: work around power outage: how much do we need to warm up the incubator to keep it from going below a certain threshold?
Explain how it relates to previous setup.

## Slide 20: What-If Simulations: Example
Plan Power Outage
Estimated Intervention Time with Best Config
Best Ctrl Configuration
Current Ctrl Configuration

## Slide 21: Two-way Communication
Physical Twin
Plant
Controller
Digital Twin
Communication
3D Visualization
Safety Monitoring
Predictive maintenance
Fault Diagnosis
Support for decision making
...
Self-reconfiguration
Notes: Physical twin modified to accept new values for parameters of the controller.
  But safe limits to these have been hard-coded.
  More safety issues remain…

## Slide 22: Self-Adaptation Example
Physical Twin
Digital Twin
RabbitMQ
Controller
Kalman Filter
State
Model
What-If Simulation
New Configuration
Configurator
H=40.0
C=10.0
Digital Twin
3D Visualization
Safety Monitoring
Predictive maintenance
Fault Diagnosis
Support for decision making
Self-reconfiguration
Notes: Warnings:
New configurations must be triple checked before being applied.
Controller must always have hard-coded safety checks.

## Slide 23: Complex Self-Adaptation Example
Start when object is placed inside the incubator.
Schedule experiment to gather relevant data
  E.g., let the plant cool down to a safe temperature, then ramp up heating for some time.
Configure controller for the new experiment
Gather experiment data
Run parameter estimation for new experiment
Re-configure Kalman filter with new parameters
Run What-if simulations to optimize controller behavior
Re-configure controller
Data Recorder
Kalman Filter
Anomaly Detector
Configurator
LSE Solver
What-If Simulation
Configurator

## Slide 24: Research Questions
Physical Twin
Plant
Controller
Digital Twin
Goals:
3D Visualization
Safety Monitoring
Predictive maintenance
Fault Diagnosis
Support for decision making
...
Self-reconfiguration
What-If Simulation
Configurator
Data Recorder
Kalman Filter
LSE Solver
Anomaly Detector
RQ1: Are these the atoms of a digital twin?
RQ2: How to describe their orchestration to accomplish complex tasks?
RQ3: How to quickly engineer new digital twins?
Visualizer
Moving Average

## Slide 25: Ongoing Case Studies
UR Robot Arm
  Developed with Emil Madsen and Carlos Hansen
  Modelling and parameter estimation done.
  Linearization of the model for KF done.
Desktop Robotti
  Mirgita is doing safety monitoring using Gazebo and co-simulation (acting as DT)
  Mathias working on indoor position tracking with cameras on the robot.
  Bachelor students built a more detailed calibrated model.

## Slide 26: Related Ongoing Work
RabbitMQ FMU
  One way communication into what-if co-simulations.
  Thule, Casper, Cláudio Gomes, and Kenneth Lausdahl. “Formally Verified FMI Enabled Data Broker: RabbitMQ FMU,” SummerSim ’20. Virtual event: ACM New York, NY, USA, 2020.
Tracking Simulator and PyFMU:
  Legaard, Christian Møldrup, Cláudio Gomes, Peter Gorm Larsen, and Frederik F. Foldager. “Rapid Prototyping of Self-Adaptive-Systems Using Python Functional Mockup Units,” SummerSim ’20. Virtual event: ACM New York, NY, USA, 2020.
Python Interface to COE (to run What-if Co-simulations)
Fault injection in Co-simulations
  e.g., simulate network effects.
High-performance Co-simulations
Parallel co-simulations in DSE in cluster

## Slide 27
Cláudio Gomes, Hao Feng, Casper Thule,
Kenneth Lausdahl, Peter Gorm Larsen